## Slide 1
Authors: Jad Zalzal, Laura Minet, Jeffrey Brook, Cristian Mihele, Hong Chen and Marianne Hatzopoulou
Date: January 6, 2025
Bridging CTM and Land-Use Regression:
A High-Spatial Resolution Approach to Simulate Air Pollution Exposure Disparities Under Major Transportation Policy Scenarios

## Slide 2: Emissions from the transportation sector
Slide #2/13
~ 23% of NOx emissions are from on-road transportation
Buses (Mostly diesel fueled)
Cars (Mostly gasoline fueled)
Trucks (Mix of gasoline for light-duty trucks and diesel for medium and heavy-duty trucks)

## Slide 3: Disparities in exposure to LDV and truck NOx emissions in Toronto
Regions with higher residential instability and higher ethnic concentration had higher emissions from trucks and LDVs
Slide #3/13
Zalzal, J., & Hatzopoulou, M. (2022). Fifteen Years of Community Exposure to Heavy-Duty Emissions: Capturing Disparities over Space and Time. Environmental Science & Technology, 56(23), 16621-16632.
Check out the paper here:

## Slide 4: CTMs vs LURs
Slide #4/13
Chemical Transport Models (CTMs)
Land Use Regression Models (LURs)
vs
Suitable for simulating emission scenarios
Coarse spatial resolution
High-spatial resolution and can capture intra-urban variability
Cannot be used to simulate emission scenarios
Previous studies have shown that coarser resolution tends to underestimate disparities in exposure to air pollution

## Slide 5: Objectives
Objective 1: Model the impact of transportation emissions scenarios at a high-spatial resolution (~100m) by downscaling CTMs
Objective 2: Assess the burden of buses, cars and trucks on disparities in exposure to NO2 in the Greater Toronto Area
Objective 3: Determine the impact of spatial resolution and model used (LUR vs CTM) on exposure and environmental justice analyses
Slide #5/13

## Slide 6: Mobile measurements and CTM simulation
Slide #6/13
Mobile monitoring campaign (Shairsingh et al. 2019)
Mobile NO2 measurements collected on 30 days during the months of July and September 2015 and during January 2016 in the Greater Toronto Area (GTA)
CTM simulations
(Minet et al. 2020)
Polair3D CTM was run over 3 nested domains of 12km2, 4km2 and 1km2 resolutions for the months of May and November 2016

## Slide 7: Downscaling model
Slide #7/13
Combine CTMs and LURs for the purpose of downscaling CTM simulations under different scenarios

## Slide 8: Downscaling model
Slide #8/13
The updated downscaling factors resulted in larger decreases near major roads compared to using base case factors

## Slide 9: Base case surfaces
Slide #9/13
R2=0.73
R2=0.49
R2=0.27
R2=0.19
R2=0.24
High-spatial resolution surfaces necessary to capture intra-urban variability
LUR-based surface performed better than CTMs
NO2 surface
NAPS NO2 concentrations

## Slide 10: Contributions of different fleets to NO2 exposure
Slide #10/13
~6% of total NO2 exposure
~12% of total NO2 exposure
~14% of total NO2 exposure
Bus burden
Car burden
Truck burden

## Slide 11: Disparities in exposure to NO2
Slide #11/13
Renters, recent immigrants, visible minorities and low-income populations are exposed to higher levels of NO2
Coarse spatial resolutions underestimate disparities
Need for comprehensive policies simultaneously targeting emissions and spatial patterns of the three fleets for better EJ outcomes

## Slide 12: Summary & Conclusions
Slide #12/13
Exposure surfaces:
  High-spatial resolution surfaces performed better when compared with measurements at reference stations
  Machine learning based LUR performed better than the CTM at all spatial resolutions
  Statistically combining LURs and CTMs could be useful for generating high-resolution exposure surfaces under different scenarios
Environmental Justice:
  Renters, recent immigrants, visible minorities and low-income populations are exposed to higher levels of NO2
  Reductions in emissions from a single vehicle fleet result in a reduction in disparities but are not sufficient to eliminate them
  Coarser spatial resolution tended to underestimate disparities in exposure

## Slide 13
Check out the paper here
Let’s connect on LinkedIn!
Thank you!
Email: jad.zalzal@mail.utoronto.ca